Paper Review:

Design Modeling and Control of an Omni-Directional Aerial Vehicle (D. Brescianini & R. D’Andrea)

MAV’s are able to perform various tasks, but they are usually under-actuated i.e. unable to independently control their force and torque in all three dimensions. To achieve decoupled position and orientation control, many things were tested, but to efficiently overcome gravity, they were usually not able to fly at arbitrary orientations due to actuation constraints.

Based on these observations this paper focuses on a novel Omni-directional multi-rotor aerial vehicle with dynamical properties as independent as possible on the vehicle orientation.

The design is the result of an optimization problem. The idea is to maximize the vehicle's agility, which is defined by the maximum attainable force-torque output in any direction.

The paper proved the feasibility of the design approach and the vehicle’s capability to independently generate thrust and torque in all direction, but the simplified model to control the MAV was not able to fully decouple the vehicle’s translational and rotational dynamics.

Mechanical Design, Modelling and Control of a Novel Aerial Manipulator (A. Nikou, G. C. Gavridis & K. J. Kyriakopoulos)

Complex manipulating tasks in unstructured and dynamic environments can be achieved with UAVs and active manipulation.

This paper focuses on a small autonomous aerial robot that interacts with the environment via an end-effector by applying desired forces and torques in a 6 DOF task space.

The design is based on an optimization which tend to minimize the body volume, maximize the controllability of the system, avoid eventual aerodynamic interactions and maximize the efficiency in performing manipulation tasks.

Voliro: An Omnidirectional Hexacopter with Tiltable Rotors (M. Kamel, S. Verling, O. Elkhatib, C. Sprecher, P. Wulkop, Z. Taylor, R. Siegwart & I. Gilitschenski)

Enabling a drone to reach and hold any possible pose gives rise to many further applications such as drone-based inspection of bridges or complex camera motion for film shots. To overcome the under-actuation problem many things have been tested with fixed propellers. Some things were tested with tilting rotors MAVs and all with limited success regarding the omni-directionality of the vehicle’s.

The focus of this paper is to overcome the limitations of common commercially available multi-copters while keeping their advantages. The main idea was to place the propellers such that the counteracting forces would be as small as possible and that every propeller would contribute to the system in any configuration.

The design is an hexacopter with tiltable rotors. As the rotors orientation can be fully controlled, this system allows for decoupling the control of position and orientation.

The system provides an increased maneuverability using a control scheme based on allocation technique which achieved control with limited computation effort. However the slow dynamic of the rotor tilting motor coupled with this allocation techniques gives rise to problems.

Omnidirectional Aerial Vehicles with Unidirectional Thrusters: Analysis, Optimal Design, and Motion Control ( M.Tognon & A. Franchi)

For UAVs to interact with human unidirectional-thrust vehicles due to their under-actuation can not react instantaneously to forces with any direction. Therefore, multidirectional-thrust vehicle have been tested as a solution to overcome this problem. However, in these vehicles the set of feasible forces and torques does not span any direction in R3. Therefore omnidirectionnal thrust vehicles are in order.

This paper provides the fundamental definitions, properties and conditions needed to address the problem of omni-directional flight in the general case of n propellers.

In this paper a formalized design problem for the omnidirectional-thrust is presented. The main definitions, concepts and properties of a such design are provided.

Modeling, Control and Design Optimization for a Fully-actuated Hexarotor Aerial Vehicle with Tilted Propellers (S. Rajappa, M. Ryll, H. H. Bülthoff, A. Franchi)

Quadrotors have been used as the main platform for applications as well as research. But when it comes to physical interaction, under-actuation becomes a serious problem for the capabilities and overall stabilization of the aerial vehicle. Many attempts to overcome the underactuation problem were made with mixed results.

This paper focuses on a new mechanical design for an hexarotor, which achieve full control of the UAVs position and orientation using tilted propellers. The paper also proposes a methodology to optimize the fixed tilting angles.

The design proposed here is a modified standard hexacopter which allow for manual tilting of the propellers. These tilting angles are optimized to minimize the control input over a desired trajectory.